## Slide 1: Wind Energy Harvesting with a Kite
Antonin Bavoil¹, Jean-Baptiste Caillau¹, Lamberto Dell’Elce², Alain Nême³ , Jean-Baptiste Leroux³
1: Université Côte d’Azur, CNRS, Inria, LJAD
2: Inria
3: ENSTA Bretagne, iRDL
FGS Conference on Optimization
Gijón, June 2024

## Slide 2: Kite Electrical Energy Production (KEEP)
https://www.dailymotion.com/video/x5fwyox
KEEP is born as a follow up of Beyond the Sea®.
Idea: generate (on land) electricity with a kite.
10x less material than a wind turbine, soft.
Portable source of power in remote areas.
➝ Islands, military.

## Slide 3: Kite Electrical Energy Production (KEEP)
Approximately the same power as a wind turbine.
Currently: 10% of the production used for control.
Previous works:
  U. Ahrens, M. Diehl, R. Schmehl. Airborne Wind Energy. Springer, 2013,
  U. Fechner et al. Dynamic Model of a Pumping Kite Power System, Pergamon, 2015.
➝ Can we generate a good amount of electricity while requiring close to no control?
https://www.iksurfmag.com/reviews/kites/north-kiteboarding-evo-6m-2013/

## Slide 4: Wind Energy Harvesting with a Kite
Modelling
Numerical Results
Optimization

## Slide 5: Modelling
➝ The kite does eights in the sky to swing the arm left to right as much as possible, without tangling the lines.

## Slide 6: Modelling
As a preliminary study, we replace the control with a geometric constraint.
➝ The kite will stay on an 8-based cone centered on .
Spherical coordinates in the inertial frame :
Set of s.t.
.
➝ Like a railway track guiding a train.
Replacing the control with an algebraic constraint

## Slide 7: Modelling
State of the system in the 3d space:
  : 1D position of the tip of the arm (on a circle),
  : 2D position of the kite (on the 8-based cone).
We can do better: get through the intersection of a sphere (A, r) with a line:
Coordinates
+
➝ is enough to determine the state of the system.

## Slide 8: Modelling
How? Add a fictitious force that would result from a control.
No friction with the cone:
and
Replacing the control with an algebraic constraint
https://mathworld.wolfram.com/Cone.html
Circle-based cone

## Slide 9: Modelling
Dynamics: conservation of linear & angular momentum.
All forces apply at point (the kite):
  Gravity,
  Aerodynamical forces,
  Line tension,
  Fictitious cone force.
Compute the dynamics
Arm
Generator
Lines
Kite
Wind

## Slide 10: Modelling
Gravity force = weight of the kite + weight of the lines:
Gravity

## Slide 11: Modelling
Apparent wind: (velocity – wind).
Aerodynamical force on the kite:
Aerodynamical force on the lines, applied at point :
Aerodynamical forces

## Slide 12: Modelling
Conservation of angular momentum of the arm gives:
Hence , where is obtained by solving the dynamics cf. next slide.
Line tension & conservation of angular momentum

## Slide 13: Modelling
Recall that and .
Conservation of linear momentum gives: .
Hence . Linear in .
Solve .
Computing the explicit dynamics

## Slide 14: First Numerical Results
Assemble and using forward auto. diff. for exact, fast & maintainable derivatives:
  julia> kite_speed = jvp(u -> OK(u, params), u, du)
Runge-Kutta 5(4) (Tsitouras 2011):
➝ Cyclic behavior: toward a limit cycle…
Solving the dynamics

## Slide 15: First Numerical Results
Define a Poincaré section at where the cycle begins (arbitrary).
Dense ODE output & continuous callback allow us to save the state every time it crosses one of these hyperplanes:
➝ 2 limit cycles, interested in the one with that does not tangle the lines.
Limit Cycle
Iteration | (seconds)
1 | 2.7857519406370397
2 | 3.0933710067285087
3 | 3.0930984474625856
... | …
7 | 3.093098056921132
8 | 3.0930980569206064
Iteration | 
1 | 2.7857519406370397
2 | 3.0933710067285087
3 | 3.0930984474625856
... | …
7 | 3.093098056921132
8 | 3.0930980569206064

## Slide 16: Optimization
We define the following problem
Over with the number of available parameters to optimize.
With constraints:
  Box constraints on the state.
With final state obtained by the ODE solver.
Problem: Optimize the Average Power over a limit cycle

## Slide 17: Optimization
Augment ODE state:
  ➝ with being the cumulated work done by the generator,
  with its associated differential equation
Augment optimization variables: ➝
➝ Maximize over with constraints:
  The augmented constraint
  Box constraints over the state
Augmentations

## Slide 18: Optimization
Gradients and Hessians of the constraints computed with automatic differentiation
Initialization on the limit cycle, where constraints are satisfied
Use Interior Point OPTimizer (IPOPT)
➝ Look for saturated box constraints
➝ perform a sensitivity analysis around the optimal point
Ongoing work

## Slide 19: Conclusion
Solve the ODE ➝ find the limit cycle ➝ optimize on the limit cycle, thanks to Julia tools
Move forward to a controlled model, without the cone constraint
Have an engineer build a prototype that would (in)validate our results through measurements
K. Desenclos, 2022, Production d’électricité par voile de kite.

## Slide 20: Annex 1: Basis vectors related to the local wind
Apparent wind perpendicular to the lines:
Basis of the apparent wind:

## Slide 21: Annex 2: Forward Automatic Differentiation
Define st.
A dual number is
Define the base operations:
  …
sin, cos, exp, etc. are defined using etc.
➝ See ForwardDiff.jl